## Slide 1
State Estimation: The Inverse Problem
SVD Truncation vs Noise-Weighted Pseudo-Inverse

## Slide 2
Problem Setup
Forward model with measurement noise:
  y = A·x + n
Where:
  • y ∈ ℝᵐ — measured wavefront (Zernike coefficients)
  • A ∈ ℝᵐˣⁿ — sensitivity matrix (m > n, overdetermined)
  • x ∈ ℝⁿ — DOF state to estimate
  • n — measurement noise with covariance Cₙ = E[nnᵀ]
Goal: Estimate x̂ given measured y

## Slide 3
Approach 1: SVD with Truncation
Singular Value Decomposition of A:
  A = U·Σ·Vₕ
Pseudo-inverse:
  A⁺ = Vₕᵀ·Σ⁺·Uᵀ
where Σ⁺ = diag(1/σ₁, 1/σ₂, ..., 1/σₙ)
Problem: Small σᵢ → 1/σᵢ → ∞ amplifies noise!

## Slide 4
SVD Truncation Regularization
Truncate at index k: set σᵢ = 0 for i > k
Truncated pseudo-inverse:
  Aₖ⁺ = Vₕ,ₖᵀ · Σₖ⁻¹ · Uₖᵀ
Solution:
  x̂ₜᵣᵤₙc = Aₖ⁺ · y
Discards n−k least-constrained DOF combinations
Retains only directions producing measurable wavefront changes
Example: k=12 with n=22 DOFs → keeps 12 most important modes

## Slide 5
Approach 2: Noise-Weighted Pseudo-Inverse
Weighted least-squares objective:
  min (y − Ax)ᵀ Cₙ⁻¹ (y − Ax)
  x
Analytical solution:
  x̂ᵥᵥₗₛ = (Aᵀ Cₙ⁻¹ A)⁻¹ Aᵀ Cₙ⁻¹ y
Down-weights Zernikes/sensors with high measurement uncertainty

## Slide 6
Whitening Transformation
Equivalent approach: whiten the problem first
Define whitened quantities:
  ȳ = Cₙ⁻¹/² · y
  Ā = Cₙ⁻¹/² · A
Then solve standard (unweighted) least-squares:
  x̂ = Ā⁺ · ȳ
This is computationally more stable

## Slide 7
Combined Approach (ts_ofc)
StateEstimator combines both methods:
Step 1 — Whiten by noise covariance:
  ȳ = Cₙ⁻¹/² · y, Ā = Cₙ⁻¹/² · Ã
Step 2 — Truncated pseudo-inverse of whitened system:
  x̃ = Āₖ⁺ · ȳ
Step 3 — De-normalize to physical DOFs:
  x̂ = N · x̃

## Slide 8
Compact Formula
Combined solution in one line:
  x̂ = N · (Cₙ⁻¹/² Ã)ₖ⁺ · Cₙ⁻¹/² · y
Where:
  • N — DOF normalization matrix
  • Ã — normalized sensitivity matrix
  • Cₙ — measurement noise covariance
  • (·)ₖ⁺ — truncated pseudo-inverse (k modes)
References:
  • arXiv:2406.04656, Eq. (10)
  • Martínez-Galarza et al. 2024, ApJ 974:108

## Slide 9
Summary: Two Approaches
SVD Truncation:
  • Regularizes by discarding small singular values
  • Prevents noise amplification from 1/σᵢ → ∞
  • Keeps k most optically important modes
Noise-Weighted Pseudo-Inverse:
  • Uses measurement covariance Cₙ
  • Down-weights uncertain measurements
  • Optimal under Gaussian noise assumptions
ts_ofc combines both: whiten first, then truncate