## Slide 1
V-Modes and the OFC Control Loop
Mathematical foundations of the Active Optics closed-loop control
Vera C. Rubin Observatory — AOS Team

## Slide 2: Outline
The forward optical model: y = A x
DOF normalization
State estimation: solving the inverse problem
V-modes: definition, interpretation, and truncation
PID control in DOF space
PID control in v-mode space
Equivalent DOF-space gain and cross-coupling

## Slide 3
The Forward Optical Model

## Slide 4
Forward Model: y = A x
The sensitivity matrix A maps DOF changes to wavefront errors (Zernike coefficients) across the focal plane:
y = A · x
• y ∈ ℝᵐ — wavefront error vector (m = n_sensors × n_Zernikes = 4 × 19 = 76)
• A ∈ ℝᵐˣⁿ — sensitivity matrix, evaluated at sensor field angles and camera rotation
• x ∈ ℝⁿ — DOF state vector (n = 22 used DOFs: 5 M2 hex + 5 cam hex + 7 M1M3 bend + 5 M2 bend)
A is constructed from a double Zernike expansion of the optical model. It depends on sensor positions and the camera rotation angle.

## Slide 5
DOF Normalization
DOFs span different physical scales (hexapod μm, rotations deg, bending mode coefficients). A diagonal normalization matrix makes them comparable:
N = diag(w₁, w₂, …, wₙ)
The normalized sensitivity matrix and coordinates:
Ã = A · N ẍ = N⁻¹ · x
So the forward model in normalized coordinates becomes: y = Ã · ẍ
Normalization weights come from the range-fwhm.yaml configuration (see Martínez-Galarza et al. 2024, Eqs. 9–11).

## Slide 6
State Estimation
Solving the inverse problem

## Slide 7
State Estimation Overview
Given measured wavefront error y_meas, estimate the DOF state. Three steps:
1. Compute residual wavefront error:
y = y_meas − y_intrinsic − y₂
2. SVD truncation — discard poorly constrained modes:
Ã = U · Σ · V_h → set σᵢ = 0 for i > k
3. Noise-weighted pseudo-inverse and de-normalization:
ẍ = pinv(C⁻½ Ãₖ) · C⁻½ · y x̂ = N · ẍ
C is the measurement noise covariance (see chapters 1–6 of SITCOMTN-177). Truncation index k = 12 retains 12 of 22 v-modes.

## Slide 8
V-Modes
Definition, interpretation, and truncation

## Slide 9
V-Mode Definition
V-modes are the right singular vectors of the normalized sensitivity matrix:
Ã = U · diag(σ₁, …, σₙ) · V_h
• Each ROW of V_h is a v-mode: vᵢ = (V_h)ᵢ,: ∈ ℝⁿ
• Each v-mode is a LINEAR COMBINATION of all normalized DOFs
• σᵢ = optical leverage: wavefront change per unit of v-mode i
• V-modes are sorted: σ₁ ≥ σ₂ ≥ … ≥ σₙ
• Number of v-modes = number of used DOFs (22 with current config)

## Slide 10
V-Mode Coordinate Transformations
DOFs to v-modes:
v = V_h · N⁻¹ · x
V-modes to DOFs:
x = N · V_hᵀ · v
These transforms are exact and lossless because V_hᵀ V_h = I.
In ts_ofc: StateEstimator.get_vmodes_from_dofs() and StateEstimator.get_dofs_from_vmodes()

## Slide 11
Why V-Modes Map to Specific Aberrations
Each v-mode produces a characteristic wavefront pattern described by the LEFT singular vector uᵢ = U[:,i]:
• uᵢ contains the Zernike coefficients (across all sensors) resulting from commanding v-mode i
• If uᵢ is dominated by Z4 coefficients → v-mode i is "the focus mode"
• If uⱼ is dominated by Z11 coefficients → v-mode j is "the spherical mode"
• The SVD discovers these optical eigenmodes automatically from the sensitivity matrix
• The association is approximate: each v-mode has a dominant Zernike plus smaller contributions to others
This is why operators say "v-mode 5 is focus" or "v-mode 12 is spherical": each v-mode is the most efficient DOF combination for producing that aberration.

## Slide 12
Truncation and V-Mode Importance
The singular values σᵢ determine which v-modes are well-constrained by the measurements:
• V-modes 0 – (k−1): large σᵢ, produce measurable wavefront changes, reliably reconstructed
• V-modes k – (n−1): small σᵢ, buried in noise, discarded during state estimation
With truncation_index = 12 and n = 22 DOFs:
• 12 v-modes retained (well-constrained)
• 10 v-modes discarded (noise-dominated)
• The PID controller still operates on all 22 v-modes, but the state estimate for v-modes 12–21 is effectively zero

## Slide 13
PID Control
In DOF space and v-mode space

## Slide 14
PID in DOF Space (control_vmodes = False)
The PID operates directly on DOF estimates:
eₖ = setpoint − x̂ₖ
uₖ = K_p · eₖ + K_i · Iₖ + K_d · dₖ
• K_p = diag(kp[dof_idx]) — proportional gain per DOF
• K_i = diag(ki[dof_idx]) — integral gain per DOF
• Iₖ accumulates past errors, clipped by max_integral
• Correction applied: xₖ₊₁ = xₖ + (−uₖ) (negative feedback)
Gain meaning: kp[0] = 0.18 → "correct 18% of M2 hex dZ error per iteration". Conservative gain ensures stability despite noise and model errors.

## Slide 15
PID in V-Mode Space (control_vmodes = True)
Three steps wrap around the same PID core:
Step 1 — Project DOF estimate to v-modes:
v̂ₖ = V_h · N⁻¹ · x̂ₖ
Step 2 — PID in v-mode space:
uₖᵛ = K_pᵛ · eₖᵛ + K_iᵛ · Iₖᵛ + K_dᵛ · dₖᵛ
Step 3 — Project correction back to DOFs:
uₖ = N · V_hᵀ · uₖᵛ
Advantage: different gains per optical importance level. High gain on well-constrained modes, low gain on noisy modes.

## Slide 16
Equivalent DOF-Space Gain
Composing the three v-mode steps, the effective DOF gain is:
K_eff = N · V_hᵀ · K_pᵛ · V_h · N⁻¹
When K_p is a uniform scalar kₚ :
K_eff = kₚ · N · V_hᵀ V_h · N⁻¹ = kₚ · I
→ V-mode round-trip cancels. Identical to DOF-space control.
When K_p has two gain levels (0.18 for top 11, 0.045 for rest):
K_pᵛ = 0.045 · I + 0.135 · P₁₁
P₁₁ = projection onto first 11 v-modes. Applies uniform base gain + boost on most important optical modes. Creates cross-DOF coupling (coordinated multi-DOF corrections).

## Slide 17
Summary

## Slide 18: DOF Space vs. V-Mode Space
DOF space (control_vmodes = False)
  State = physical DOFs (hexapod positions, bending modes)
  Gain = correction fraction per physical DOF
  Simple, physically intuitive, no cross-coupling
V-mode space (control_vmodes = True)
  State = optical eigenmodes ordered by singular value
  Gain = correction fraction per optical mode
  Enables gain tuning by optical importance
  Creates coordinated multi-DOF corrections

## Slide 19: Key Takeaways
V-modes are linear combinations of normalized DOFs, discovered by SVD of the sensitivity matrix
Each v-mode produces a dominant Zernike pattern (focus, astigmatism, spherical, ...)
Singular values rank v-modes by optical leverage; truncation discards noisy modes
With uniform scalar gain, v-mode control = DOF control (round-trip cancels)
With per-v-mode gains, the system boosts important modes and dampens noisy ones
Number of v-modes = number of used DOFs (currently 22)